## Slide 1: GEANT4 simulation of the 10B-based Jalousie detector for neutron diffractometers
Irina Stefanescu1, R. Hall-Wilton1, G. Kemmerling2, M. Klein3, C.J. Schmidt3,4, W. Schweika1,2
1European Spallation Source ERIC, S-22100 Lund, Sweden
2Forschungszentrum Jülich GmbH, D-52425 Jülich, Germany
3CDT CASCADE Detector Technologies GmbH, D-69123 Heidelberg, Germany
4GSI Detector Laboratory, D-64291 Darmstadt, Germany

## Slide 2: Neutron diffraction – the bare essentials
Neutron diffraction is used to study samples that are composed of single or many different crystals (polycrystals).
d”h”k”l”
λi = 2∙ dhkl ∙sinθhkl
Debye-Scherrer diffraction cones according to Bragg’s law:
(λ – wavelength neutron, dhkl – lattice distance, θhkl – scattering angle)
dhkl
d’h’k’l’
n
detector

## Slide 3: Neutron diffraction – the bare essentials
Neutron diffraction is used to study samples that are composed of single or many different crystals (polycrystals).
d”h”k”l”
λi = 2∙ dhkl ∙sinθhkl
Debye-Scherrer diffraction cones according to Bragg’s law:
(λ – wavelength neutron, dhkl – lattice distance, θhkl – scattering angle)
dhkl
d’h’k’l’
n
detector

## Slide 4: Neutron diffraction at ESS
ESS Lund
At ESS three diffraction instruments (DREAM, MAGIC, HEIMDAL) are about to finalize the detailed design.
HEIMDAL, thermal powder diffractometer
MAGIC, single-crystal diffractometer
DREAM, powder diffractometer
Requirements for detectors for the ESS instruments:
able to handle rates as large as 4 kHz/cm2
2θ-resolution < 0.29° (< 6 mm x 6 mm pixel size)
neutron detection efficiency > 50% at 1 Å
γ-sensitivity < 10-6

## Slide 5: Neutron diffraction at ESS
ESS Lund
At ESS three diffraction instruments (DREAM, MAGIC, HEIMDAL) are about to finalize the detailed design.
HEIMDAL, thermal powder diffractometer
MAGIC, single-crystal diffractometer
DREAM, powder diffractometer
Requirements for detectors for the ESS instruments:
able to handle rates as large as 4 kHz/cm2
2θ-resolution < 0.29° (< 6 mm x 6 mm pixel size)
neutron detection efficiency > 50% at 1 Å
γ-sensitivity < 10-6
I. Stefanescu et al., Neutron detectors for the ESS diffractometers, JINST 12, P01019(2017).

## Slide 6: The Jalousie detector
“Mantel” detector
n
Jalousie detector for POWTEX (FRM2) and DREAM (ESS)
The Jalousie detector designed to fulfil the requirements of the new generation of neutron diffractometers.
Developed by the company CDT in Heidelberg, Germany.
Jalousie utilizes the 10B-technology.
The POWTEX-Jalousie mantel detector currently under construction and testing.
The design and construction of the DREAM-Jalousie mantel detector planned to start in 2018.
The results of the simulation for the POWTEX-Jalousie detector are also valid for the DREAM-Jalousie detector.

## Slide 7: The POWTEX-Jalousie detector
2.3 m
45°
Δθ=0.47°
sample
192 cathode strips
0.8 m
n
3D matrix of 16 (wires) x 192 (cathode strips) = 10240 non-identical sensitive elements per counter (voxels).
segment

## Slide 8: The POWTEX-Jalousie detector
Depth of the segment (~25 cm) chosen to allow for the interaction of each incoming neutron with up to 8 Boron-layers.
Counting gas: Ar-CO2 (80-20) in continuous flow.
ε ≈ 50% at 1 Å
M. Henske et al., The 10B-based Jalousie neutron detector – An alternative for 3He-filled position sensitive counter tubes, NIMA 686 (2012) 151.
The Jalousie segments are mounted in modules of 8.
18 detector modules to cover 2π around the sample.

## Slide 9: GEANT4 simulations for the Jalousie detector
15.6 mm
info on the energy deposited, tof, voxel ID ( voxel center) saved on file for each detected neutron.
Simulation strategy: model the readout voxels as trapezoids made of Ar-CO2 gas
~8 mm x 7 mm x 15.6 mm
tof
Ei+1
Ei
voxeli
voxeli+1
o
o
o
o
n + 10B  7Li + α
Info needed on the creation and propagation of the electron avalanches and their collection by the anode wire.

## Slide 10: Validation of the GEANT4 model for Jalousie
GEANT4
FWHM = 8.1 mm
FWHM =7.85 mm
FWHM = 12.5 mm
strip with width 7.22 mm
FWHM = 12.8 mm
Experimental results obtained in measurements with collimated beams
G. Modzel, PhD thesis, Univ. of Heidelberg, 2014.
(wire pitch = 12.6 mm)

## Slide 11: GEANT4 simulations for the Jalousie detector
Chart: Wavelength (Å)
| 0.5 | 1.0 | 1.8 | 2.0 | 2.5 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0
eff, all events | 37.456 | 55.088 | 66.044 | 67.45 | 69.638 | 70.54 | 71.88 | 72.28 | 72.596 | 73.094
eff, threshold = 100 keV | 33.25 | 48.618 | 58.52 | 59.774 | 61.432 | 62.516 | 63.774 | 64.278 | 64.53 | 64.964
 simulated efficiency for the POWTEX-Jalousie mantel detector > 50% at 1 Å
GEANT4
CAD design for the POWTEX/DREAM Jalousie detector

## Slide 12: GEANT4 simulations for the Jalousie detector
Δd/d = instrumental resolution
(resolution function)
Δd/d
WISH@ISIS, experimental,
NaCaAlF sample
At spallation sources: Δd/d = Sample ⊗ Instrumentation
moderator, beamline components, detector

## Slide 13: GEANT4 simulations for the Jalousie detector
 study the detector contribution to the resolution function by comparison to a reference detector

## Slide 14: GEANT4 simulations for the Jalousie detector
 study the detector contribution to the resolution function by comparison to a reference detector

## Slide 15: GEANT4 simulations for the Jalousie detector
 study the detector contribution to the resolution function by comparison to a reference detector
Use the Vitess neutron trajectories as input for the GEANT4 ParticleGenerator.

## Slide 16: GEANT4 simulations for the Jalousie detector
 study the detector contribution to the resolution function by comparison to a reference detector
*WISH: world-class powder diffractometer operational at the ISIS (UK) spallation source.
Jalousie detector
WISH-like detector*
(3He-tubes)
GEANT4
Use the Vitess neutron trajectories as input for the GEANT4 ParticleGenerator.

## Slide 17: GEANT4 simulations for the Jalousie detector
POWTEX-Jalousie detector, GEANT4
WISH-like detector,
GEANT4
WISH, experimental
Main diffraction peaks and their relative intensities well reproduced by the model.

## Slide 18: Conclusions and outlook
The implementation and validation of the GEANT4 model for the Jalousie mantel detector (POWTEX/DREAM version) almost completed.
Focus is now on using the detector model to predict the physics performance in real experiments.
The Jalousie detector is the baseline technology for the single-crystal diffractometer (MAGIC) and the thermal powder diffractometer (HEIMDAL) at the European Spallation Source. Both detector designs will be optimized in GEANT4.

## Slide 19: GEANT4 simulations for the Jalousie detector
POWTEX-Jalousie detector, GEANT4
WISH-like detector, GEANT4

## Slide 20: GEANT4 simulations for the Jalousie detector
Chart: Wavelength (Å)
| 1.8 | 3.0 | 4.0 | 6.0 | 10.0
POWTEX-Jalousie | 6.209 | 10.304 | 13.86 | 20.956 | 34.672
WISH, 3He tubes, 8 mm diameter, 15 bar | 4.567 | 7.83 | 10.489 | 15.265 | 26.74
o
o
o
o
Δtofdet
d ~ 15 mm
10B4C layers
~8 mm
d ≤ 8 mm in current tof detectors used for power diffraction studies (e.g., thin ZnS scintillators or 3He-based gas counters)
For POWTEX (L = 20 m), Δtofres-chopper = 10 μs  Δtof/tof ≈ 0.15%.
ESS: DREAM: L = 76 m, MAGIC = 171 m, HEIMDAL = 168 m.