## Slide 1: Remote Handling Electrical and fluid couplings
Erik Nilsson
Mechanical Engineer
ESS Chopper Group
www.europeanspallationsource.se
20 November, 2017

## Slide 2: Quick on routing
Cables routed in two sections
  Flexible section (change part)
  Fixed section
Bulkhead connector between flexible and fixed section
Utilities routed in three sections
  Self supporting snorkel
  Flexible section
  Fixed section
Connector requirements applicable on fixed end
More information and discussion tomorrow
Notes: Routing
  Avoid access limitations to remote handling interfaces.
  Maintenance connectors within 200mm of the bottom of the bunker roof shielding.
  Utilities routed in three sections
    Self supporting snorkel
    Flexible section
    Fixed section
Bundling
  The cables and utilities shall be collected in appropriate bundles.
  Larger collected connectors preferred over multiple connectors.
Connectors
  Minimise exposure to radiation during connection/disconnection.
  Push-pull type of connectors with lanyard pulls are preferred.
  “Breakaway“ plugs in bayonet type connector are a possible secondary choice.
  A fully integrated, fully remote handling plate is required if manual actuation is not possible.

## Slide 3: Electrical connectors
Appropriate bundles.
Module specific bundles.
Fast manual actuation connectors are sufficient.
Push-pull type connectors with lanyard pulls preferable
  LEMO B Series [FNG] (stainless steel with PEEK contact isolators)
Bayonet type connectors is acceptable
Activation of connector might be an issue.
  Local shielding?
LEMO B Series (Lanyard pull)

## Slide 4: Fluid connectors
Water
  Double shut-off connector
  Button for disconnection
  Stäubli RBE (Stainless steel 316L)
Pneumatic
  Button for disconnection
  8mm nominal diameter (11mm possible)
  Stäubli RBE (Stainless steel 316L)
Vacuum
  ISO-KF flange with clamp
  Stainless steel flexible hose
Gas
  Double shut-off connector
  Button for disconnection
  Stäubli RBE (Stainless steel 316L)
  Stäubli RBE (quick release) series

## Slide 5: Discussion
What level of standardisation is reasonable and achievable?
What sizes and types of connectors do you envision?
Notes: Activities restricted to
  Extraction (RH-I and RH-II)
  Reinstallation (RH-I)
  Inspection and/or realignment of component/module (if required)
Complex RH activities shall be avoided.
  Reduced design complexity
  Reduced construction cost
  Reduced tooling cost
No in-situ RH maintenance is foreseen.
  Modules/components stored on site during cool down.
  Exchange of a module for a spare unit will be the quickest method to repair (hot-swap).