## Slide 1: Remote Handling Guide positioning, extraction and realignment
Erik Nilsson
Mechanical Engineer
ESS Chopper Group
www.europeanspallationsource.se
20 November, 2017

## Slide 2: Floor stability issue
Guide positioning not RH activity per say (no maintenance or reliability issues).
Only extraction (yellow zone)
Floor stability causes realignment of guides to become a RH activity.
Expected floor stability in bunker region:
  +-3mm
Notes: Activities restricted to
  Extraction (RH-I and RH-II)
  Reinstallation (RH-I)
  Inspection and/or realignment of component/module (if required)
Complex RH activities shall be avoided.
  Reduced design complexity
  Reduced construction cost
  Reduced tooling cost
No in-situ RH maintenance is foreseen.
  Modules/components stored on site during cool down.
  Exchange of a module for a spare unit will be the quickest method to repair (hot-swap).

## Slide 3: Guide RH requirements in Yellow zone
Realignment of guide in Z-direction
Remote extraction of guide section
50 micro precision in installation (and realignment)
Adaptable to different types of guide solutions
  Interfaces to choppers and other components

## Slide 4: Concepts
Three point kinematic mount
  Secured by two bolts (one in each end)
Extraction
  Guide rods or rollers required
Re-alignment
  Screw transferring force to “hidden” alignment point. Other two points are visiable.
Notes: Activities restricted to
  Extraction (RH-I and RH-II)
  Reinstallation (RH-I)
  Inspection and/or realignment of component/module (if required)
Complex RH activities shall be avoided.
  Reduced design complexity
  Reduced construction cost
  Reduced tooling cost
No in-situ RH maintenance is foreseen.
  Modules/components stored on site during cool down.
  Exchange of a module for a spare unit will be the quickest method to repair (hot-swap).

## Slide 5: Discussion
Other concepts?
Ways forward?
  General common concept
  Instrument specific
  Transfer requirements to suppliers and let them handle it
Notes: Activities restricted to
  Extraction (RH-I and RH-II)
  Reinstallation (RH-I)
  Inspection and/or realignment of component/module (if required)
Complex RH activities shall be avoided.
  Reduced design complexity
  Reduced construction cost
  Reduced tooling cost
No in-situ RH maintenance is foreseen.
  Modules/components stored on site during cool down.
  Exchange of a module for a spare unit will be the quickest method to repair (hot-swap).