## Slide 1: The Life of a Beam Transport Module for the ESS Project
Keith Middleman
STFC Daresbury Laboratory
ESS Particle Control CDR, Lund, 29th November 2017

## Slide 2: Overview
Daresbury Vacuum Overview:
  Large scale facility designs and experience
  ISO9001
  Cleaning
  Baking
  Vacuum acceptance
  Cleanroom
  Particle control
  Controlled venting and evacuation
Notes: Well defined UHV specs

## Slide 3: Synchrotron Radiation Source (SRS)
CLRC Daresbury Laboratory
Synchrotron Radiation Department
Vacuum Support Group.
Ultra High
Vacuum Guide
A compendium of Proceedures and Specifications
<Issue 3>
©CLRC Daresbury Laboratory,1996

## Slide 4: 3 Onsite Accelerators
EMMA
ALICE
VELA

## Slide 5: International Vacuum Design of Accelerators
DIAMOND
KATRIN
ELI-NP

## Slide 6: Vacuum/Mechanical specifications
CLRC Daresbury Laboratory
Synchrotron Radiation Department
Vacuum Support Group.
Ultra High
Vacuum Guide
A compendium of Proceedures and Specifications
<Issue 3>
©CLRC Daresbury Laboratory,1996
Notes: Well defined UHV specs

## Slide 7: Quality Control Documentation
Vacuum documents include 3 process documents:
  Proc-001 – Calibration of Total Pressure Gauges
  Proc-002 – Calibration of Residual Gas Analysers
  Proc-003 – Measurement of Thermal Outgassing
And 8 specification documents:
  Spc-001 – General Definitions
  Spc-002 – General specification for UHV
  Spc-003 – Cleaning of vacuum items
  Spc-004 – Leak Testing of Vacuum vessels
  Spc-005 – Acceptance tests for vacuum vessels
  Spc-006 – Acceptance tests for clean mechanical pumps
  Spc-007 – Material for Vacuum Flanges
  Spc-008 – Standard Vacuum Notes
Notes: Well defined UHV specs

## Slide 8: Beam Transport Module requirements
STFC design
ESS Vacuum Requirements:
  1 x 10-9 mbar
  UHV Cleanliness
  Particle free to ISO 5 or better
To design, procurement and assemble;
  2 Differential pumping systems
  74 LWUs, 52 Beampipes
Vacuum requirements within STFC Vacuum Specs & will include:
  Cleaning
  Baking
  RGA Scanning
  Particle counting
Notes: ESS design on LHS is still to be done, RHS is STFC design`

## Slide 9: Mechanical drawings referencing STFC specifications
Notes: Well defined UHV specs

## Slide 10: Vacuum Vessel Acceptance
There are 2 main methods that STFC have used over the years to ensure that STFC mechanical and vacuum specifications are met:
  1) Allow manufacturer’s to strictly adhere to our specifications and conduct factory visit and acceptance tests
  2) Allow manufacturer’s to manufacture vessels (STFC still conducts factory visits) and ensure the completed vessel has a suitable leak rate and then ship back to STFC for all further processing to be done
STFC has successfully used options 1 and 2 over the years, however, no manufacturer’s have the infrastructure or facilities STFC has in house.
Option 2 allows STFC to maintain greater control over the processes and provides better quality control over the vacuum specifications.
Option 2 has been implemented for the ESS BTM work package
Notes: Word the last 2 bullet points more carefully

## Slide 11: Assembly locations & Facilities
Engineering technology centre
Notes: Engineering technology centre

## Slide 12: ISO 9001
Job cards completed upon entry to vacuum laboratory
Job card remains with vacuum component through all stages of the process as a record
Notes: Engineering technology centre

## Slide 13: Database starting point

## Slide 14
Information extracted from the paper Form

## Slide 15: The electronic form completed as tasks undertaken

## Slide 16
email sent to customer and archive to confirm job completion

## Slide 17: Cleaning Process
Auto washers for small items
Power wash booth for large items
Full detailed procedure in ASTeC spc-003 - Cleaning of vacuum items

## Slide 18: Solvent wash, HFE72DE
1 x Automatic solvent
cleaning plant, model F100.
2 x Solvent cleaning plants:
Model E1500 – 1500mm x 500mm x 500mm
Model S3000 – 3000mm x 600mm x 500mm
70% Trans-dichloroethylene,
10% Ethyl nonafluorobutyl ether,
10% Ethyl nonafluoroisobutyl ether,
5% Methyl nonafluorobutyl ether,
5% Methyl nonafluoroisobutyl ether.

## Slide 19: Solvent Cleaning
Alkaline degreaser
Vapour Stage

## Slide 20: Cleaning Process Scientifically Developed
Publications:
K.J. Middleman, J.D. Herbert, R.J. Reid, Vacuum 81 (2007) p793-798
J.D. Herbert and R.J. Reid, Vacuum, Vol. 47, 6-8, p693 (1996)
J.D. Herbert, R.J. Reid, A.E. Groome, J. Vac. Sci. Technol. A12(4), p1767, (1994)
Considered aqueous and solvent based cleaning solutions
Considered main gas loads in an accelerator – Thermal outgassing and stimulated desorption
Conclusions
  Aqueous cleaners suitable only for thermal outgassing and not stimulated desorption
  Solvent based cleaners produced better results
  HFE (Hydrofluoroether) based solvent performed best, even better than our previous solvents

## Slide 21: Drying
Hot drying cabinet.

## Slide 22: Vacuum Laboratory
4 x ovens to 250oC
vacuum furnace to 1100oC
Air oven to 150oC
Leak detection & test facilities.

## Slide 23: Bakeout
Beampipes baked to 250oC for 24 hours
LWU’s with BPM’s welded in only bakeable to 50oC. Discuss?

## Slide 24: Vacuum Ovens
General Vacuum oven,
250oC, 1 x 10-10 mbar.
Vacuum furnace, immersion bake,
1100oC, 1 x 10-8mbar.

## Slide 25: How do we accept vacuum vessels?
Pre and Post bake RGA scan
RGA scanning at temperature
Leak testing
Pressure Region* | Typical Leak Rate (mbar l sec-1) | Typical Outgassing Rate (mbar l sec-1 cm-2) | Comment
Low Vacuum | 10-2 | 10-4 | Outgassing rates not usually relevant in this region
Medium vacuum | 10-5 | 10-7 | 
High Vacuum | 10-7 | 10-9 | 
Very High Vacuum | 10-9 | 10-11 | 
UHV | 10-10 | 10-13 | 
XHV | <10-12 | <10-15 | Special techniques required to measure leak and outgassing rates

## Slide 26: How do we accept vacuum vessels?
Vessel acceptance is based upon the RGA analysis, a vessel is clean if:
The residual gas spectrum shall have been recorded over 1 –200 amu
The spectrum shall have been corrected for sampling error, mass discrimination and species relative sensitivities (see Appendix 3)
These limits are expressed in terms of percentages of the total pressure in the system, corrected as indicated
The definition of “general contaminants” is the sum of the partial pressures of all peaks present in the residual gas spectrum of mass to charge ratio (amu) equal to 39, 41-43 and 45 and above (excluding any above 45 specifically listed in the table below). Also to be excluded from this summation are any peaks related to the rare gases xenon (i.e. 132, 129, 131) and krypton (i.e. 84, 86, 83)
Pressure Region | General Contaminants (%) | Perfluoropolyphenylethers Sum of (peak at 69 and 77 amu) (%) | Chorinated species (Sum of peaks at 35 and 37 amu) (%) | Comment
UHV | 0.1 | 0.01 | 0.01 | Assuming system baked. Calculation to be done at 10-9 mbar or below
HV - UHV | 0.75 | 0.075 | 0.075 | Assuming system unbaked. Calculation to be done at 10-7 mbar or below

## Slide 27: Vacuum vessel acceptance
After acceptance of the vacuum component it will be vented with pure ‘dry’ filtered N2
Filtered down to 0.1µm
‘Dry’ - N2 purged until a dew point of -70⁰C is measured, keeping moisture down to acceptable low levels
Vessel is capped and remains under a N2 atmosphere

## Slide 28: Use foil?
In general we wrap all ‘clean’ vacuum components and they are labelled
Protects clean items.
  Indicates cleaned items.
For particle control foil is bad
  Shed particles of all sizes.
For particle controlled ‘clean’ vacuum components we only use ‘clean’ plastic caps and NO foil

## Slide 29: Cleanroom

## Slide 30: Low particulate experience on ALICE
ALICE Photoinjector vessel
In ISO 4 Cleanroom

## Slide 31: Particle counting procedures
A one minute sample of particle level should then be taken and checked to ensure it meets the ISO 5 standard. If it does not then the chamber should be left for a further 30mins and the area retested. If it is still not below the required level then the chamber should be moved back out to the changing area and re-cleaned with a lint free wipe and blown down with N2.
The chamber then should be un-flanged, to do this remove all but two bolts from the flanges (note: this will produce an increase in the particle count) then let the chamber settle again and take another one minute particle count. Then remove the flanges and take a one minute area sample to check ISO class.
If ISO 5 is not achieved wait a further 30mins and take a further sample. Repeat this upto 5 times. If the area still does not reach the required level the chamber should be removed and the process re-started.
Once the area is acceptable blow the internal chamber surfaces with filtered N2 at 7 bar. The chamber should then be tapped delicately a number of time across the surface with a rubber mallet. This, N2 blow then tapping procedure, should be repeated twice more.
Then take a one minute sample at the location specified for the unit whilst purging at 0.5 bar with filtered nitrogen. This should be done remotely if possible.
Repeat stages 4&5 four more time, recording the counts each time.
If each of the particle counts in stage 5 meets the ISO5 specification seal/cap the vessel – passed
If any of the particle counts in stage 5 do not meet ISO5 repeat another 5 times, if vessel repeatedly fails then speak to area supervisor.

## Slide 32: Cleanroom Upgrade
Change area 6m2 - ISO 7
Outer area 80m2 - ISO 6
Inner area 12m2 ISO 4 at rest
ISO 5 with 2 people
Change area 6m2 - ISO 7
Outer area 80m2 - ISO 5
Inner area 12m2 ISO 3 at rest
ISO 4 with 2 people

## Slide 33: Cleanroom Upgrade
High and Low pressure feeds for the particle counting process.
Automatic switch over when N2 runs low
One set at 5-7 bar, one at 0.5-1.5 bar

## Slide 34: Cleanrooms
Once all vacuum work in the vacuum laboratory is completed the vessel or component is then transferred to the area outside the clean room and prepared for the cleanroom
Vessels are wiped down with tack cloths
All surfaces cleaned and wiped down with IPA wipes
Vessels blown off with high pressure filtered N2
Allow time for any particles to settle and then open doors for transfer into the clean room
Vessels are transferred into the outer area of the cleanroom – ISO5 and are left for a number of hours before they enter the main ISO3/4 assembly area

## Slide 35: Changing room.
Sanitise & moisturise

## Slide 36: How do we do it?
Wands designed and made specifically for the LWU’s.
PTFE end on with holes drilled to force the N2 backwards
Wand with specific angle designed to push the N2 from the central chamber back towards the ends

## Slide 37: LWU Particle Counting Preparation
Blow down with high pressure N2, then repeat with gentle mallet tapping. Repeat process 3 times.
Switch to low pressure N2 then perform particle counts WITH mallet tapping (worst case scenario) until ISO5 achieved.
Repeat particle counts WITHOUT mallet tapping until ISO 5 achieved

## Slide 38: How do we do it?
Particle counts to be taken in 4 positions
Measure particle count
Measure particle count
Purge vessel with 4 m/s bar N2
Measure particle count
Particle counts to meet ISO 5 on 5 consecutive occasions before moving to the next position
Purge vessel with 4 m/s bar N2
Measure particle count

## Slide 39: Procedures

## Slide 40: Beampipe Particle Counting
Blow down with high pressure N2, then repeat with gentle mallet tapping. Repeat process 3 times.
Switch to low pressure N2 then perform particle counts WITH mallet tapping (worst case scenario) until ISO5 achieved.
Repeat particle counts WITHOUT mallet tapping until ISO 5 achieved
Measure particle count

## Slide 41: Particulate counting
Unfiltered
12 mins
of filtering
later.
Resultant data file to be saved to database

## Slide 42: SAES NEXTorr Particle Counting
Chart: After NEG Activation Second Blow
| 0.3 | 0.5 | 1 | 5 | 10 | 25
Upside Down - after neg activation | 0 | 35 | 0 | 0 | 0 | 0
Side facing left - after neg activation | 71 | 0 | 106 | 0 | 0 | 0
Side facing right - after neg activation | 0 | 35 | 0 | 0 | 0 | 0
Upright - after neg activiation | 0 | 0 | 35 | 0 | 0 | 0
Chart: After NEG Activation Third Blow
| 0.3 | 0.5 | 1 | 5 | 10 | 25
Upside Down - after neg activation | 0 | 0 | 0 | 0 | 0 | 0
Side facing left - after neg activation | 71 | 0 | 0 | 0 | 0 | 0
Side facing right - after neg activation | 0 | 0 | 0 | 0 | 0 | 0
Upright - after neg activiation | 0 | 35 | 35 | 0 | 0 | 0
Chart: After NEG Activation First Blow
| 0.3 | 0.5 | 1 | 5 | 10 | 25
Upside Down - after neg activation | 3142 | 2259 | 1447 | 177 | 282 | 177
Side facing left - after neg activation | 1095 | 494 | 388 | 0 | 35 | 0
Side facing right - after neg activation | 530 | 424 | 424 | 0 | 0 | 0
Upright - after neg activiation | 3142 | 2259 | 1447 | 177 | 282 | 177

## Slide 43: Pumping Carts
Controlled pumpdown and venting using the carts shown.
One is permanently located in the cleanroom, the other in the assembly area.

## Slide 44: Summary Report
1-2 page summary after all vacuum processes complete
Printed particle count results to included with the report along with the job card

## Slide 45: STFC Delivered