## Slide 1: Mechanical design of B10 based technology neutron detectors
Isaak Lopez Higuera
on behalf of the ESS Detector Group
www.europeanspallationsource.se
November 28, 2017

## Slide 2: ESS Detector group and Event Formation Groups and Friends
People: Mostly funded by EU grants
ESS HQ Lund: 22 people
Linkoping: 4 people
Daresbury: 4 people
CERN: 1 person
Collaborations with 30 groups across EU
Facilities:
Mechanical workshop (Embla)
Detector workshop (Utgård, 790 m²)
Source Facility (at Lund University)

## Slide 3: Outline
The need for a new detector technology
B10 technology
  Coatings
  Mechanical design engineering work
  Multi-Blade
  MB15
  MB16
  MB16SS and test at RAL
  MB future plans (Integration design for ESTIA/FREIA)
  Multi-Grid
  MG24 and iterations
  MG.CNCS
  MG.SEQ
  Integration design for CSPEC

## Slide 4: New detector technology
Why a new detector technology:
Shortage of He3 gas
Affordable large area detectors
Better counting rate capability
Best alternative...B10 detectors
Large area
Low cost
Modular
High total efficiency
Many layers – lower local rate
No need for resistive readout – low gain
He3 supply demand graphic
ESS detector’s rate capability needs graph

## Slide 5: B10 detectors as alternative to He3
Several blades to increase efficiency
+ 2.97 MeV
blade
α
ArCO2 atmosphere

## Slide 6: Detector Coatings Workshop - Linköping
CemeCon CC800/9 ”Chewbacca” – industrial DC magnetron sputtering machine
2 runs/day (~1.7 m2 1 μm 10B4C/run ) 800 - 900 m2 per year
Linköping univ logo?
Good adhesion | 0.5-10 μm on Al, Si, Al2O3
High Density | 2.45 g/cm3
High 10B content | 79.3%
Low residual stress | 0.09 GPa at 1 mm 10B4C on Si
Multi-Grid inner blades hanging
Chewbacca opened view
target

## Slide 7: The mechanical design engineering work
n
B10 MWPC test
Multi-Blade
Multi-Grid
n
n

## Slide 8: Multi-Blade Multi-Blade detector technology for ESS instruments
The Multi-Blade will be used in the reflectometers ESTIA and FREIA
Detector requeriments:
High instantaneous rate capability: 100 kHz/mm2
High spacial resolution: 0.5mm
FREIA
ESTIA
 | FREIA | ESTIA
Wavelength | 2.5-12 | 4-10
Sample-detector | 3m | 4m
Max instantaneous flux kHz/mm2 | 100-200 | 100-500
Size x (mm) y (mm) | 300 300 | 500 250
Instruments layout at ESS
x100 state of the art
x3 state of the art

## Slide 9: Multi-Blade How it works: the physics behind the Multi-Blade
Blades oriented in a 4m radius and inclined 5˚
Knife shaped converter (coated)
Efficiency 45% at 2.5Å
Cassette assembly
n

## Slide 10: Multi-Blade How it works: Cassette assembly

## Slide 11: Multi-Blade demonstrators
Concept introduced in 2005
Proof of concept in 2012
Institut Laue-Langevin
University of Perugia
Institut Laue-Langevin
4 cassette demonstrator

## Slide 12: Multi-Blade demonstrators MB15
First demonstrator at ESS
100x140mm active area demonstrator
Overall size 480x380mm
MB15 without front lid
MB15 isometric view

## Slide 13: Multi-Blade demonstrators MB16
360˚ access to the detector
Different thickness windows (0.5, 1, 2mm)
Overall size 420x260mm
MB16 vessel
MB16 expanded view

## Slide 14: Multi-Blade demonstrators MB16SS and test at RAL
More compact 300x190mm
Electronics outside:
- Easy access to hem
- Less pollution of Ar, heat generation
MB16SS assembled
MB16SS expanded view
Titanium blades
1mm 2mm 3mm

## Slide 15: Multi-Blade demonstrator MB16SS and test at RAL
n
Tested at RAL, in a horizontal reflectometer
Use of a goniometer, ±18˚ of rotation
Set up for the test at RAL
Installation for the test at RAL
MB16SS
18˚
Wedge
Table
Neutron beam
Goniometer
2.3m

## Slide 16: Multi-Blade demonstrator MB16SS and test at RAL
Not a dead area but the overlap avoids dead zones
BNi mask

## Slide 17: Multi-Grid Multi-Grid detector technology for ESS instruments
CSPEC
T-REX
 | CSPEC (cold) | T-REX (thermal/bispectral)
Sample-detector distantce | 3.5m | 3m
Typical initial λ, Å (meV) | 2 to 15 Å (20 to 0.36 meV) | 0.7 to 6.4 Å (160 to 2 meV)
Detector coverage, deg | -30 to 140 +-26 | -30 to 150 -15 to +25
Detector area | 29m2 | 21m2
The Multi-Grid technology will be used in the spectrometers: CSPEC and T-REX
Instruments layout at ESS

## Slide 18: Multi-Grid How it works: Grid
Layer thicknesses for cold spectrometer optimization used at MG.CNCS and applies to CSPEC(16 blades):
7 blades 0.5μm,
7 blades 1.0μm,
3 blades 1.5μm
For thermal optimization 20 blades total:
4 blades 1.0μm,
10 blades 1.25μm,
6 blades 2.0μm.
Column assembly
Grid
n
The MultiGrid detector design was invented by the ILL and is jointly developed by the ILL and ESS

## Slide 19: Multi-Grid How it works: column assembly
n

## Slide 20: Multi-Grid demonstrator MG24 and iterations
MG24: First demonstrator
MG24.Copper: Test with low α
MG24.T: Optimized for thermal neutrons
MG24.Alu foil: Test with foil window

## Slide 21: Multi-Grid MG.CNCS and test at SNS
Tested in CNCS instrument at SNS
-2 columns of 48 grids
-3mm thickness window
-Detector area 1150x185mm²
3He tubes
n

## Slide 22
Crystal
Incident beam
Reflected beam at Ei = 17.20meV
Reflected beam at Ei = 13.74meV
He3
Multi-Grid MG.CNCS and test at SNS
MG
He3
MG
High rate
High rate

## Slide 23: Multi-Grid demonstrator MG.SEQ: Installation proposal at SNS in the SEQUOIA instrument
Test with thermal/epithermal neutrons
First large area detector under vacuum
Mounted in the lower bank ~5m and 25˚ from sample
˞ 1m² of detection area
View of SEQUOIA instrument with MG.SEQ in green
SEQUOIA instrument

## Slide 24: Multi-Grid demonstrator MG.SEQ: Installation proposal at SNS in the SEQUOIA instrument
9 columns, 40 grids in each
Telescopic sliders to access grid assemblies
Use of inclined wedges so all grids are at the same distance from the sample
1050 x 914 x 450mm
neutrons
MG.SEQ isometric view
MG.SEQ top view

## Slide 25: Multi-Grid demonstrator MG.SEQ: Installation proposal at SNS in the SEQUOIA instrument
3mm thickness window
8 rows of 17 rods, Ø3mm
Full access only from 1 side
n
MG.SEQ bottom view
Total deformation

## Slide 26: Multi-Grid demonstrator MG.SEQ: Installation proposal at SNS in the SEQUOIA instrument
Amplified 50 times
Max deformation: 1.2mm on the sides
Max equivalent stress: 176 MPa
Stress in the rods: 80 MPa
Equivalent stress in the vessel
Equivalent stress in the rods
Amplified 50 times

## Slide 27: Multi-Grid Detector for CSPEC
Neighbour vessels configuration, minimizing dead spaces, 21mm from grid to grid
Integration of the detector vessels in the CSPEC instrument
Vessel length: 3.5m
Detector configuration: 2 columns per vessel (column width 153.5mm)

## Slide 28: Future steps
Multi-Blade
MB17 with 300mm converters, size of FREIA
- Already coated Titanium blades of this size successfully
Work in the integration with ESTIA
Multi-Grid
Finalize the design of MG.SEQ
Keep working towards the instrument specific design for the CSPEC and T-REX instruments

## Slide 29: Thanks!!
Horizon 2020 grant agreement 676548

## Slide 32
Vertical Reflectometer
Horizontal Reflectometer
Reflectometry at ESS: FREIA and ESTIA

## Slide 33: Multiblade
MB16 SS and test at RAL: Results
 | Multi-Blade
gas gain | 20
efficiency | 45% @ 2.5Å 56% @ 4.2Å 65% @ 5.1Å
spatial resolution | 0.5 x 2.5 mm2
uniformity | 10%
overlap | 50% eff. drop in 0.75mm gap
stability | <1% in 12h
counting rate capability | >1.6 kHz/mm2 (lower limit) >17kHz / channel (lower limit)
gamma-ray sensitivity | < 10-7 (with 100keV threshold)

## Slide 34: Multi-Grid demonstrator MG.SEQ: Installation proposal at SNS in the SEQUOIA instrument
Intermediate PCB layer, separates both atmospheres
Groove in the cover to guide flat cables to the PCB layer
Electronics plugged to the PCB layer
    Mesytec 128 channel front-end
    Preamp, shaper, multiplexer
    60 x 140 x 20 mm3
    1 per detector module
    9 required in total
3mm thickness window
8 rows of 17 rods, Ø3mm
n
n
MG.SEQ bottom view
MG.SEQ section