## Slide 1: T-REX: Vacuum Tank and Detector Integration Status
Detectors and Data Acquisition for Instruments Meeting - Paris, 12th February 2018
Nicolò Violini, Tadeusz Kozielewski, Jörg Voigt, Earl Babcock, Zahir Sahli, Helmut Soltner, Günter Kemmerling, Klaus Bussmann, Frank Suxdorf, Thomas Brückel, Andreas Wischnewski
Hans Kämmerling,
Mario Koenen,
Achim Heynen
Andrea Orecchini, Alessandro Paciaroni, Marco Zanatta, Pietro Tozzi, Francesco Sacchetti

## Slide 2: Outline
T-REX instrument overview
Requirements for Detectors
Vacuum tank design status
Detectors vacuum/mechanical integration

## Slide 3
small energy gaps, excitations in the parent compounds of high Tc SC,
excitations into the Stoner continuum.
Conductivity is governed by coupling mechanism between between phonons and ion diffusion
QENS: ps to ns dynamics governs biological functionality
T-REX: INS for a broad community

## Slide 4
Bispectral:
  Neutron guide optimised for
  thermal
  Cold extraction does not
  compromise thermal
Chopper cascade:
  Flexible configuration
  Resolution  flux
  < 24 RRM pulses
50 % detector coverage
in 1st day
162m <336 Hz
108m <252 Hz
40 m
32 m
+Provision of T0 at 19 m
2 meV < Ei < 160 meV
@ 2MW ESS:
  (3x 4-SEASONS, 6xIN5 ) x n.of useful RRM spectra
T-REX unique with 5D mapping
Polychromatic experiments

## Slide 5
Sample-detector distance: 3 m ± 1 mm
Large solid angle: vertical -15° to +25°
horizontal +1° to +70° (project scope)
Minimum angle: 1°
Time resolution (FWHM): ≤ 5 µs
PSD Positional resolution (FWHM): 20 mm x 20 mm x 10 mm
Detection Efficiency: ≥ 70 % at 1.8 Å
average 74 %, 1.6 Å < λ < 5 Å
Count Rate: <104 Hz/cm2
Neutron Selectivity: <10-6 gamma detection prob.
Noise: <10-4 events/s/cm2
Vacuum ≤ 10-6 mbar
Prevention of secondary scattering
~ 20 m2
Functional Requirements
Scattering Characterization System
-36° to +144° (full scope)

## Slide 6
Detector vacuum vessel - Status
Status: iteration with FEM calculations on final design, working on tender docs and specs for TG3
31.03.18 open call for tender
31.10.18 contract signed
Q3.19 completion of manufacturing
(tbd) Q4.19 – Q3.21 delivery at ESS
Allocated budget seems OK
Open questions/discussions:
Integration of primary beam collimators
Sample change system tests
Detectors Design + vacuum interface + utilities + installation/maintenance strategy
Design and Procurement of vacuum system

## Slide 7
10-6 mbar
Stainless steel 10 mm
50 T of material
Height 3250 mm
Diameter 8500 mm
Volume 85m3
Magnetic req.
2m R from sample (may be too expensive)
Access from lateral door
Inside:
Primary collimator,
Holding field,
PASTIS / SEE,
Radial collimators,
Detectors,
Get lost tube, beam stop
Detector vacuum vessel – Design characteristics

## Slide 8: Vacuum system for Detector Vessel
pumps
4 roots
3 turbo
1 screw
1 cryo
< 2 h to restore

## Slide 9
Sample exchange system
Enables faster sample/SEE change
Mechanically decoupled
Design+construction work is done independently
Need for a sealing test

## Slide 10
Multi-GRID detectors (baseline)
Prototype under construction
20-24 10B4C layers
6 x 1 µm, 10 x 1.25 µm, 4 x 2 µm
to reach 45-48% efficiency @ 1Å
Fairly compares to 3He at 6 bar
Pure Al frames
MG @ CNCS
Size = half of “8-pack” module
Installation June-July 2016
Test at spectrometer
Operation for 6+ months
Side-by-side comparison to 3He
User experiments

## Slide 11
1mm gap
2mm gap
20 columns
96 rows
Multi-GRID detectors (baseline from TG2 Mar ’17)
Full scope needs
100 modules = 5 banks x 20 modules
Project scope
40 modules = 2 banks x 20 modules
CNCS
prototype

## Slide 12
Detectors Vacuum integration box

## Slide 13
4 columns per box (A and B)
window
web plates
side plates
6 columns per box (C and D)
Detectors Vacuum integration box

## Slide 14
The preliminary stress analysis was performed for 4 different layouts:
4-columns per box, 3 mm web plates, 8 mm side plates
4-columns per box, 2 mm web plates, 8 mm side plates
6-columns per box, 2 mm web plates, 8 mm side plates
6-columns per box, 2 mm web plates, 10 mm side plates
++ option C, the influence of neighboring, closely mounted :
1 mm gap between neighboring boxes
1 bar pressure gradient
A detailed stress proof according to design rules to be applied was not yet done.
Investigated layouts
Detectors Vacuum integration box

## Slide 15
Considered aluminum alloy: AlMg4.5Mn0.7
Elastic modulus: 70 GPa
Poisson’s ratio: 0.33
Yield stress: 125 MPa
Tensile strength: 275 MPa
Strain to rupture: 15%
Weld properties coefficient: 1.0
Joint coefficient: 0.85
Stress Criteria Sm: 83.3 Mpa
Yield point for limit analysis: 70.83 Mpa (= 0.85 · Sm)
Material Properties

## Slide 16
Loads
B: symmetry conditions for ½ model
C / D: only used to numerically fix the model

## Slide 17
Results - deformations

## Slide 18
Results – elastic stresses

## Slide 19
Results – elastic stresses (details)

## Slide 20
Results – plastic strains for limit analysis with RL=70.83 MPa

## Slide 21
Neighboring boxes – 1mm gap
0.5mm – closed gap
Deformations, mm
Contact pressure, MPa
Elastic stresses, MPa
Plastic strain (limit analysis), mm/mm
symmetry

## Slide 22
Mechanical Integration of the boxes
TOPAS
Design