## Slide 1
China initiative Accelerator Driven System (CiADS)
Institute of Modern Physics
Yuan He, Hushan Xu, Bin Zhang

## Slide 2: Outlines
Motivation and Project Introduction
Design and Progress
  Accelerator
  Target
  Reactor
Summary

## Slide 3: Nuclear Power Development in China
Nuclear energy is an inevitable strategic option to meet China energy demand in the future
  China is the largest energy consumer in the world and coal is the major resource for electricity production (79% in 2011)
  China claims that the CO2 emissions will reach a peak around 2030 while Paris Climate Agreement.
Current status of China nuclear power
  37 nuclear power reactors in operation, 20 reactors under construction
  Produced electricity: 591TW.h, 3.56% share in 2016
The planned NP development in China (-2020)
  By 2020, the installed nuclear capacity will be increased to 58GWe (~7%), and 30GWe are under construction
  By 2050, 350~400GWe (~20% ), comparable with the total NP capacity in the world (391GWe, 447 reactors in 2017).
Notes:     almost same scale of the total capacity in the world todays!

## Slide 4: Issues for Sustainable NP
Management and safe disposal of nuclear waste
  1GWe PWR ~25 ton/year;
  ~2200 ton/year in 2030 in China; ~10000 ton/year now in the world
  Total capacity of Yucca Mountain ~ 70000 ton;
Accelerator Driven Sub-critical Reactor and Accelerator Driven Recycle of Used Fuel are promising path to resolve the problems.
“The ADS has the advantage that it can burn pure minor actinides while avoiding a deterioration of the core safety characteristics.”
⎯ ADS and FR in Advanced Nuclear Fuel Cycles – A Comparative Study, NEA/OECD, 2002

## Slide 5: Basic Principle of ADS
Accelerator
Spallation target
Transmu-tation
neutron
Output power
Sub-FR

## Slide 6: ADS Roadmap in China
Inject I
Inject II
2014
~2.5 MeV
&10mA
2016
~25 MeV
&~10mA
<2030
~1.0 GeV
&<15mA
~203x
~1.0 GeV
&>15mA
10 MWt
>500 MWt
≥1 GWt
10 MeV
￥1.78 B
Phase I
2011--2016
Phase II
2017--2024
Key Tech. R&D : Acc., Target, Blanket… Prototypes
Initial Facility
Demo. Facility
Phase III
Phase IV
Indust. Facility
2024
~500 MeV
&~10mA
“strategic Priority Research Program” of the Chinese Academy of Sciences
CiADS

## Slide 7: CIADS Project (2017-2024)
Approved in Dec. 2015
Leading institute: IMP
Budget: >1.8B CNY (Gov. and Corp.)
Location: Huizhou, Guangdong Prov.
Contribution Partners: CIAE, CGN, IHEP, CASHIPS, etc.
China initiative Accelerator Driven System (CiADS)
Location is in Huizhou city, Guangdong Province, 73 km away from Huizhou and 140 km away from Shenzhen. The site is on the top of hill, latitude is around 150m, facing the South See and backing on the mountain. The High Intensity Heavy Ion Accelerator Facility (HIAF) is in the same campus.

## Slide 8: Technical routes of CiADS
Acc
Target
Reactor
HE
proton
spallation
neutron
Superconducting linac, >2.5MW
Granular W solid, >2.5MW
Sub-reactor, LBE, 10MW
Current limit >100mA, CW
CiADS
ADS
Heat exchange out of reactor
Thermal shock free
Liquid metal, high conductivity
Good natural circulation ability
fission
energy

## Slide 9: Overall Arrangement of CiADS
① SC linear accelerator
② Coupling beam line
③ Reactor Hall
④ RF High power station
⑤ Beam dump and target exp.
⑥ Cryogenic station
⑦ Accelerator assembly Hall
⑧ SC resonator conditioning hall
⑨ Cooling water station
⑩ Target assembly and exp. hall
⑪ Hot cell building
⑫ Electric transform station

## Slide 10: Top Level Specifications of CiADS
ADS | 
Heat Power of ADS | 10 MW
Superconducting Linac | 
Species | Proton
Beam Energy | 500 MeV
Beam Power | ~2.5 MW
Operation mode | CW/pulse
High Power Target | 
Materials | Tungsten, granular flow
Neutron Flux | 1016~17 /s
Heat Power | ~2.5 MW
Subcritical Reactor | 
Heat Power driven by beam | ~7.7MW
Fuel and enrichment | 19.75% UO2
Keff | 0.73

## Slide 11: Outlines
Motivation and Project Introduction
Design and Progress
  Accelerator
  Target
  Reactor
Summary

## Slide 12: General design of CiADS linac
CIADS sc-lianc design concept：
RAMI dependent design
Beam loss ＜0.1 W/m
Optimization overall
Rt front end: beam quality control and re-built
Sc-linac: high redundancy, compensation
Beam on target: homogenies scanning
Specials at transport sessions:
ion | proton | 
energy | 500 | MeV
current | 5 | mA
frequency | 162.5/325/650 | MHz
operation | CW&pulse | 
Beam loss | ＜0.1 | W/m
length | 367.52 | m
Beam dynamic configuration

## Slide 13: Session design of linac

## Slide 14: SC resonators of CiADS
f (MHz) | 162.5
βopt | 0.101
Epeak / Eacc | 5.9
Bpeak / Eacc | 12.1
G = Rs×Q0 (Ω) | 28.4
R / Q0 | 153
Q0 (4.4K, Rs=71.4 nΩ) | 4E8
Vacc (MV) | 0.78
Epeak (MV/m) | 25
Bpeak (mT) | 50
Pdiss(W) (4.4K, Rs=71.4nΩ) | 10
HWR010
VTA results of HWR010
fabrication
f(MHz) | 162.5
Vacc(MV) | 1.8
Bpeak(mT) | 40
Epeak(MV/m) | 32
R/Q(Ω) | 292
G（Ω） | 51
Eacc(MV/m) | 6.6
P(W)(Rs=70nΩ) | 16
βopt | 0.15
Q0 | 7.2E+08
HWR015
VTA results of HWR015
String assembly in cleanroom

## Slide 15: SC resonators of CiADS
f (MHz) | 325
βopt | 0.42
Epeak / Eacc | 3.78
Bpeak / Eacc | 7.09
G = Rs×Q0 (Ω) | 108.5
R / Q0 | 420.8
Q0 (2K, Rs=20 nΩ) | 5.4E9
Vacc (MV) | 5.4
Epeak (MV/m) | 35
Bpeak (mT) | 70
Pdiss(W) (2K, Rs=20nΩ) | 12.8
DSR042
Double Spoke
Single Spoke
CH
Operating Frequency (MHz) | 650
Operating Temperature （K） | 2
Geometrical beta βg | 0.63
Optimal beta βopt | 0.67
Number of cells | 5
Eacc at βopt (MV/m) | 15.6
Epeak / Eacc (βopt) | 2.25
Bpeak / Eacc (βopt) | 4.79
G (Ω) | 192.7
R / Q0 | 360
Q0 | 1E10
Vacc at βopt (MV) | 11.39
Cavity Length (m) | 1.09
Elliptical 063

## Slide 16: Prototypes of Cryomodules
HWR
Spoke

## Slide 17: Prototype of ADS sc-linac
25 MeV
10 mA
25 MeV ADS Front-end Demo sc-Linac
World first ADS front-end demo lianc.
First 25 MeV CW beam of 170 uA, and pulse beam of 12.6 mA in 2017.
The beam of 10 MeV@2 mA, the most powerful CW proton from sc-linac, were demonstrated in 2016.

## Slide 18: Outlines
Motivation and Project Introduction
Design and Progress
  Accelerator
  Target
  Reactor
  Material
Summary

## Slide 19: General design of granular target
item | value
Beam energy | 250~500 MeV
Beam current | 5~10 mA
Neutron flux | 1016~17/s
Effective Neutron | 2~6.2 n/p
Exchange power | ~2.5 MW
Granular flow | <72 m³/h
Lifter hight | ~40 m
function
Remove beam heat
Yield neutron
Coupling A & R
Lifter
Coupling area
Heat exchanger
Cont-ainer
Purifier
Emergency container
Notes: 靶系统回路循环运行，在靶段耦合发挥功能，在其他功能段从热工、材料等角度冗余支持运行。

## Slide 20: Granular Target Conception
It can stands for tens of MW beam power
Increasing flexibility to use other target materials to increase the neutron yields
Spallation
neutron
Sand Clock
Merits:
Heat exchange outside
No Stress due to beam trip
No thermal shock due to beam pulse
Drawbacks：
Dusty due to abrasion
Science China
Tech. Sci. 58(10)
July 2015
Granular flow
Beam heating

## Slide 21: Granular Target Materials
 | value
gradients | 93W-4.5Ni-2.5Fe
diameter | 1.0±0.1mm
density | 17.6g/cm3
impurity | ≤0.1%
ductility | ≥10%
Alloy W/Ni/Fe has high neutron yield, mechanical performance, high thermal conductivity, low thermal expansion, low cost, etc.
Neutron yield
Heat deposition
hardness
Produce 13 tons
Abrasion line

## Slide 22: Prototype of granular target
Electro-magnetic lifter
Heat exchange exp.
Integral target setup, verify granular flow, heat exchanger, electro-magnetic lifter, purifier, and so on
Granular flow
Granular temp.
Water temp.
Flux with aperture

## Slide 23: Design of A. & T. coupling
 | value | unit
Emit. RMS norm. (x/y/z) | 0.28/0.28/0.33 | π mm.mrad
Entrance αx/αy/αz | 1/1/-1 | ——
Entrance βx/βy/βz | 20/20/20 | mm/π.mrad
Beam profile on target | round | 
homogenity | ±10 | %
99.99% beam diameter | <110 | mm
bending
collimation
differential
bending
scanning

## Slide 24: Design of A. T. R. coupling
Vacuum differential session
Scanning
A T R coupling
High Vacuum
10-5 Pa
Low Vacuum
0.1 atm
FR with central tube
Thermal insulation between target and reactor
Non hard connection and touch between target and reactor container
Windowless from Acc to Target
Donna type scanning to uniform temperature rising
Monitoring beam on target
Physical de-coupling and neutron coupling

## Slide 25
Exp. of E-Beam on W Granular Target
2014.7, e-beam tungsten target coupling setup
Identify Target Power Density of proton beam 1.0GeV@10~20mA on W
Long-term operation stably
Granular flow and heat simulation agree with experiment

## Slide 26: Outlines
Motivation and Project Introduction
Design and Progress
  Accelerator
  Target
  Reactor
Summary

## Slide 27: General Design of FR
 | Top level spec.
type | LBE sub- FR
Power | 10MWt (incl. beam)
fuel | UO2 (19.75%)
Main coolant Configuration | Pool-loop
Main coolant driven mode | Forced circulation
Coolant | LBE
Main coolant pressure | Normal
Main coolant temp | 280-380℃
main coolant exchanger | Main exchanger×2 Auxiliary exchanger×4
Main pump | Mechanical pump×2
Secondary Loop coolant | Pressure water
Secondary Loop pressure | 1.4MPa
Secondary Loop Temp | 225-260℃

## Slide 28: Neutronics design
UO2 Enrichment 19.75% Fuel；
Lifetime 3 years
Parameters | Unit | Value | 
 |  | BOL | EOL
Reactor Power | MW | 7.74 | 7.66
Target Power | MW | 2.26 | 2.34
Proton Energy | MeV | 500 | 
Beam Intensity | mA | 4.51 | 4.67
Neutron Yeild | n/p | 8.81 | 
Uranium Load | t | 1.7217 | 
EOL Burnup | MWd/tU | 4902 | 
Keff | - | 0.73457 | 0.72687
Ks | - | 0.76922 | 0.76450

## Slide 29: Thermo-Hydraulic Design
Limitation：
The highest temperature of cladding is 460℃< limitation 550℃
The highest coolant velocity is 0.36m/s< limitation 2m/s
The highest temperature of fuel is 534℃
Coolant flow distribution of 7 rods bundle
Name | Value
Power | 7.74 MW
Number of Assembly | 30
Inlet Temp | 280℃
Out Temp | 380℃
Core total flow rate | 541 kg/s
Coolant Velocity | 0.32 m/s
Highest Temp of Coolant | 456℃
Core Pressure Drop | 0.0030 MPa

## Slide 30: CiADS Safety Analysis
Reactor System Node Diagram
Accident Choose
Typical LBE reactor accidents：
Loss of flow
Blockage
Typical ADS accidents：
Beam trip
Beam overpower
Tools
RELAP5mod4.0
Replace original pressure-drop and heat relationships
Import external source driven model
It is convinced that this reactor design has great safety margin under all of the accident conditions.

## Slide 31: Typical accident safety analysis
Loss of flow
Blockage
The highest temperature of cladding is 746 K while all of the coolant flow have been lost without any safety protection system response in the reactor.
The highest temperature of cladding is 905 K while 90% reactor has been blocked.
If 1.0E8 times beam trips had been occurred during the lifetime of the reactor, cladding fatigue would happen.
Beam trip
Great heat transfer margin has been considered in this design
Beam overpower

## Slide 32: Nuclear Assembly Design
Locking
Machine
Bottom nozzle
Balance weight
Undersupport lattice
outer sleeve
Fuel bundle
Upsupport lattice
Top nozzle
Handling head
The structure of the nuclear assemble has been included Locking Machine, balance weight, bottom nozzle, under support lattice etc.
To guarantee the stability of the assembly in the reactor, locking machine and balance weight have been chosen in this design.
Name | Unit | value
Bundle number | 60 | 
Configuration | Triangle | 
Assemble length | mm | 3310
Rod length | mm | 1340
Locate mode | wire | 
Wire diameter | mm | 1.4
Assemble gap | mm | 4

## Slide 33: Coolant System Design

## Slide 34: Neutron Verifications
Online dual fiber detector and Solid track detectors
Independent Development Reactor operation monitoring system
For critical mass,
theoretical value and experimental value differ 0.3%
Target material | Period method/mk | MCNPX/mk | Relative error/mk
Tungsten particles | -0.932 | -0.99 | -0.058
Tungsten | -1.144 | -1.162 | -0.018
Lead | 1.322 | 1.562 | 0.24
Experiments verified The accuracy of target-reactor coupling calculation and core design
Built at the end of 2016（ CIAE+IMP）

## Slide 35: LBE Loop & Oxygen Control System
Oxygen control setups
LBE Loop
Built several LBE circuit research loops, achieved the precise control of oxygen concentration.

## Slide 36: Outlines
Motivation and Project Introduction
Design and Progress
  Accelerator
  Target
  Reactor
Summary

## Slide 37: Summary
CiADS is worldwide first facility of Accelerator Driven System. It has been approved and breaking ground in this year.
CiADS will demonstrate the technologies on high power linac, granular target, LBE sub-critical FR, and the high power coupling among them.
The prototypes of ADS key tech. such as front-end of sc-linac, granular test stand, and large-scale LBE loop have been built and operated. The feasibilities are verified.

## Slide 38
Thanks！