## Slide 1: SC-RFQs: towards CW high power proton linacs
G. Bisoffi (replacing A. Pisent) for the INFN-LNL Team

## Slide 2: CW RFQs
PIAVE (SC)
HI, 0,6 MeV/A, 5 mA, 80 MHz, 2 m, 280 kV, 0,5 kW
Focusing  main quadrupolar E
Acceleration  small but effective E‖
modulation of 4 vanes (synchronous with
beam bunches) one modulation period = bl
SPIRAL2 (NC)
d, 3 MeV, 5 mA, 88 MHz
5 m, 110 kV, 180 kW
IFMIF (NC)
d, 5 MeV, 130 mA, 175 MHz
10 m, 80-130 kV, 450 kW
First beam today - 4:45 pm local time! 13 mA, 300us, 1 s

## Slide 3: Outline
The PIAVE S-RFQs and precursors
Design and construction highlights
Q-curves, alignment, f&A locking
Recent upgrades of PIAVE S-RFQs
S-RFQs vs N-RFQs for high-I linacs

## Slide 4: Precursors
Stony Brook: 6 indep.-phased 50 MHz sc RFQ-lets (Pb/Cu model)
Es,p~10 MV/m global thermal breakdown
LANL: 194 MHz 4-vane, full Nb
model (for high-I beams)
ANL-1990: 64 MHz, full Nb device
ANL: 194 MHz full Nb
model, not tested
Es,p=128 MV/m CW!
Not completed…

## Slide 5: PIAVE, Bunching+2 S-RFQ’s (80 MHz)+8 sc QWR’s Full Nb, Es,p~ 25,5 MV/m, Limit: field emission
From ECRIS on 350 kV HV platform up to b = 0.05
Operational
since 2006

## Slide 6: A positive ion injector for a HI SC linac
SC
Booster
ALPI
XTU-Tandem
Positive Ion Injector
PIAVE
It injects a CW SC-linac with CW beams of higher A and Ib (A~100 is Tandem VdG stripper limits)

## Slide 7: PIAVE Injector Layout
Two S-RFQs
ECR + LEBT
n.8
QWRs
to ALPI

## Slide 8: Two S-RFQs in a cryostat
beam
line
SRFQ2
1.38 m
0.74 m
SRFQ1

## Slide 9: PIAVE RFQ design values
Designed for A/q=8,5 from an ECR on a 315 kV platform
Acceptance (norm) = 0.8 mm mrad
Output long. Emittance = 0.7 ns keV/u

## Slide 10
B
SRFQ1
SRFQ2
Lens
Lens
Si
FC
S-RFQs: setup for beam acceleration
After extensive source+LEBT setup…

## Slide 11
Df = 137°
(theoretical 0°)
T ~ 30 %, as expected from the theory
T ~ 30 → 68% (expected : 70%) after switching on the 3H-buncher
SRFQ2 is scanned, while SRFQ1 = k

## Slide 12: Outline
The PIAVE S-RFQs and precursors
Design and construction highlights
Q-curves, alignment, f&A locking
Recent upgrades of PIAVE S-RFQs
S-RFQs vs N-RFQs for high-I linacs

## Slide 13: Design and technical choices
Vane shaped electrodes: 4-pole field distortion reduced
Four rod type (-50% in volume  cryostat size)
Inductance  Stems (simple and smooth) Hmax ~ HC/3 at Eacc,nom
90°-apart-stems : H/2 on thicker vanes
Design compromises between requirements
of N-RFQs and sc resonators
EB-welded full Nb (Es,m=25 MV/m)
low rth (75 W/mK)  3 mm thick Nb sheets, filled with He
Not Nb/Cu sputtering (further R&D)
0.8 m

## Slide 14: Construction and tuning process
f300K to f4K: need to predict vacuum, cooldown, BCP Df ! Full-scale SS technological prototype developed
DL and DC-tuning
Annealing (DESY)
EB Welding (Zanon SpA)
BCP (CERN)
HPWR (INFN)

## Slide 15: f-sensitivity to vacuum, cooldown, BCP
Slow tuner range at 4K,
Dz=± 2,5 mm
Slow f-tuning from
in/out deformation
of 2 Nb/Cu sputtered
end plates (RF joint
tighness is crucial
H=3÷6 mT)
Vacuum
Cooldown
BCP
End plates in Nb/Cu

## Slide 16: Outline
The PIAVE S-RFQs and precursors
Design and construction highlights
Q-curves, alignment, f&A locking
Recent upgrades of PIAVE S-RFQs
S-RFQs vs N-RFQs for high-I linacs

## Slide 17: The main issues of S-RFQs, besides getting the right fres…
Q curve specs: Es,p=25,5 MV/m @ Pcav ≤ 10 W
Alignment: among the vanes and and between RFQ and beam axis (better than ± 0.2 mm for good beam transmission)
Keep frequency locking to M.O. vs slow volume changes (drifts of the liquid He P) and fast vibrations (and Lorenz detuning)

## Slide 18: Unloaded Q curve: nominal Ea @ Pcav ≤ 10 W achieved

## Slide 19
Bs at the joint between Nb-sputtered end-plate and Nb cavity: 36 mT
Tight contact + differential contraction: Nb/Cu plate and Nb cavity get pasted together (no gasket!)
Any looser or imperfect contact lead to substantial Q0 drops
E.g.: machining of the end-plate had to compensate for the 100 mm step on the Nb cavity due to BCP
(QBCS = 1.5x1010)
Q0-limit: rf contact at end-plate joints

## Slide 20: Conditioning Field Emission

## Slide 21: 4K-Conditioning of last multipacting levels

## Slide 22
Alignment among the vanes
Bead-pulling - DE/E < 0.4 %
fd,1 = 100.6933 MHz
fd,2 = 100.9633 MHz
Da ~ 75 mm
After EBW of the 4 quadrants, TIG welding of the Ti ribs is the very last crucial f-tuning / fine alignment step.

## Slide 23
Specs: ± 0.2 mm between SRFQ1
and SRFQ2 and between SRFQs
and injection line for good T
The quad in front of SRFQs
is moved vertically and
horizontally around the
SRFQs’ axis
Alignment between RFQ and
beam axis (better than 0,2 mm)

## Slide 24: f-locking vs slow (drifts of the liq-He P) and fast (vibrations) events
SLOW PHe DRIFTS
Mechanical tuner coping with the Df/Dt,
induced by DPHe/Dt
Cryo-plant operation minimizes DPHe/Dt
MICROPHONICS EXCITATIONS
Rigid mechanical design
Use of VCX fast tuners (ANL)
Gentle cryo-plant operation

## Slide 25: Sensitivity to He bath P variations -48 and -39 Hz/mbar
DP/Dt ≤ 5 mbar/min is required

## Slide 26
up to30 mb/min

## Slide 27
< 1÷2 mb/min
P changes smaller in range and speed after optimizing the cryo-plant parameters
Careful setup of the P.I.D. parameters controlling cryostat valves opening (continuous filling mode). Control of additional heating or increased production rate of liquid He vs cavity rf power.
Cryo-Plant Specs met: 1.2 ±0.05 bar; DP/Dt < 2 mbar/min → 1.33 Hz/s
Cryogenic-Plant Specs: 1.2 ±0.05 bar;
DP/Dt < 2 mbar/min → 1.33 Hz/s

## Slide 28: EM frequency Locking versus Mechanical Vibrations
During accelerator operation, synchronicity with beam bunches is required, hence f0 - jitters need to be controlled (Q0=8x108 & f0 = 80 MHz  Df = (f/Q0) = 0.1 Hz - sensitive to mechanical vibrations !)
Design: Ti stiffening cage (lowest mechanical mode > 120 Hz)
Operation: use of VCX fast tuners (collaboration with ANL)
Overcoupling with a 1 kW RF amplifier gives Df = 20 Hz;
VCX fast tuners can control a Df = 100 Hz range
(1)
(2)
Frequency range = ±50 Hz
Loop voltage = 300 V
Loop current = 30 A
Preact = 9 kVA
Pdiss ~ 20 W

## Slide 29
On-line Q-curves (loaded by VCX)

## Slide 30: Piezo detection of vibration during unlocking events
Room for improvement for future SRFQs: from tuning on the «drum-like» end-plates to SC plunger tuner (D. Longuevergne et al., Proc of IPAC13, 884-888)
Spectra were taken on SRFQ2 (at 4K) support bars: stable locked (green); out-of-lock (black); while losing lock (red). Spectrum of a 29 [Hz] and multiples: plate vibration modes.

## Slide 31: Lorenz force detuning
Df=-0,9 Es,p2

## Slide 32: In operation for 10 years: typical beams for users
However: SRFQs’ reliability
and performance had to be improved

## Slide 33: Outline
The PIAVE S-RFQs and precursors
Design and construction highlights
Q-curves, alignment, f&A locking
Recent upgrades of PIAVE S-RFQs
S-RFQs vs N-RFQs for high-I linacs

## Slide 34: Scope of the 2016-2017 Upgrade
IMPROVED TUNING SYSTEM - Slow tuners with non linear zones; fast tuner with perishable elements and … vanishing know-how
HIGHER FIELDS - SRFQ2 limited to 80% of the field specs (Es,p=21 vs. 25,5 MV/m) → achieve 100% of Es,p to accelerate larger A/q beams
IMPROVED ALIGNMENT - LASER tracking alignment of SRFQs on beam line, to improve beam transmission;
BETTER GAS He DRAINING - Increase the He gas flow, to make RF conditioning more efficient;
REPLACE DAMAGED COMPONENTS - heating resistors, T sensors, He and N level meters (damaged in 10 years)

## Slide 35: Combined slow+fast tuning scheme
Parallelogram (4-arm linkage):
- a long bar bound to the cavity frame;
the other long bar to the tuning plate beam port.
a short arm hosts a PT actuator
Room T slow tuning curves: linear and
repeatable, with acceptable backlash.
(shown f-offsets compensate cool down
frequency-shifts)
Notes: Four-arm linkage (parallelogram) with a long bar bound to the main cavity frame, the other one to the tuning plate beam port. A short arms hosts a PT actuator (length varied depending on fres). The opposite one is moved by an endless screw, actuated by a stepper motor. The tuning plate can be deformed by the stepper motor for coarse/slow movements and the PT-actuator for fine/fast ones.

## Slide 36: Piezotuning…
SRFQ2 VCX Tuning window between on and off statuses of the PDS.
PT static tests done at 300 and 4K
VCX FT kept operational, after
Replacing broken capacitors, diodes, fuses, …
Dynamic fres response vs actuator voltage needed to design the PT control loop (soon…)

## Slide 37: Smoother VCX loaded Q-curves
Light BCP done at CERN (13 and 16 um). Df=+45 kHz (SRFQ1), +24 kHz (SRFQ2), well within the 150 kHz slow tuning range (else Q0~1x109). Smoother curves, better He gas draining!
Stably locked at 120% of nominal Es,p; beam operation at 0,95 * nominal Es,p , very stably on a 3-days long shift. Then regular and reliable operation started again.

## Slide 38: Outline
The PIAVE S-RFQs and precursors
Design and construction highlights
Q-curves, alignment, f&A locking
Recent upgrades of PIAVE S-RFQs
S-RFQs vs N-RFQs for high-I linacs

## Slide 39: Are SRFQs applicable to high-I linacs?
An example: a SRFQ for a d-SC linac
For a d-beam, they must be kept well below 1% for RP reasons.
In a SRFQ they are even more severely limited by the heat deposition allowed in the cryostat.
Fortunately the large transverse acceptance of SRFQs allows to design a beam dynamics with very small losses.
Beam losses
Pisent, G. Bisoffi et al.,
Proc. Linac06,
227-231
Notes: As a second possible application we considered an SRFQ as first element of a 3-5 mA deuteron cw superconducting linac. Accelerators of this kind (final energy ~40MeV), for the production of neutrons and RIBs, are under construction in at least two laboratories. They require a cw RFQ that, being nowadays normal conducting, has a power consumption comparable with the rest of the linac for a rather modest beam power. An SRFQ in this case, operating in a system where a cryogenic system is anyway present, beside reducing the power consumption, allows to decrease substantially the beam losses and to increase the linac input energy (allowing a more robust beam dynamics).
Indeed for a deuteron RFQ beam losses should be kept well below 1% for radiation protection reasons. At the same time in a SRFQ the beam losses are even more severely limited by the heat deposition allowed in the cryostat (~20W). But fortunately the large transverse acceptance of SRFQs allows to design a beam dynamics with very small losses. In Tab. 5 a possible set of parameters is shown. The beam losses are <10-3 ; in Fig. 9 the PARMTEQM simulation is shown, where the very large space between beam envelope and structure aperture can be appreciated.

## Slide 40: Beam dynamics
x (cm)
y (cm)
f-fs (deg)
w-ws (deg)
Cell number

## Slide 41: RF design of a 4 m long S-RFQ in 3 modules
HFSS Results:
  Quadrupole frequency fq = 88.061 MHz
  Next quadrupole f = 95.6 MHz
  Dipole frequency fd = 94.191 MHz
  Surface electric field Es = 18.1 MV/m
  Maximum B field Bmax = 213 Gauss
  Voltage flatness = ± 0.8 %
  B field at joint location: <3 Gauss
  for a +10 mm strip

## Slide 42
Lower P: 5 mA and 2,6 MeV → Pb,m=13 kW PRF,N-RFQ~313 kW at mains;
PRF,S-RFQ~13,5 kW at mains.
T= 99,9% (strong focusing,
large acceptance,
far vanes).
Hs,p is modest.
Conversely, N-RFQs
are limited in Hs,p (Rsh is limited).
Higher modes are far away.
In N-RFQs, large tuning windows, needed to move the dipole mode away, create several areas of large consumption.
Pros
of S-RFQs
Notes: These cw RFQs, being nowadays normal conducting, have a power consumption comparable with the rest of the linac for a rather modest beam power.
Particles close to the separatrix may be lost but tend to go straight due to the transeverse focusing channel, so they are lost after exiting the SRFQ!

## Slide 43
In RFQs, for p and d, to achieve the nominal Es,p field is mandatory.
PRF is large: a quench may couple more
power into the cavity (sharp
transition to NC state).
Provide early quench
detection.
Beam power loss.
3. Liquid He boiloff →
global heating and transition to NC state.
With 5 mA-2,6 MeV ( ≥ * 2 margin) Pb,m=13 kW
and Tb = 99,8% (≥ * 2 margin vs. simulations),
Pb,lost~26 W (=cryogenic load) – Up to 40 W OK in PIAVE ! likely more.
Option: use pressurized He-II (transfer Pdiss beyond the lambda plate)
Cares to
be taken
Notes: These cw RFQs, being nowadays normal conducting, have a power consumption comparable with the rest of the linac for a rather modest beam power.
Particles close to the separatrix may be lost but tend to go straight due to the transeverse focusing channel, so they are lost after exiting the SRFQ!
Quando viene raffreddato sotto i 2,189 K a pressione normale, il cosiddetto punto lambda, diventa un superfluido conosciuto come elio liquido II
Pengo: bisognerebbe usare He-II a 1 bar, non come quello di LHC che è a 50 mbar ed è un misto delle due fasi liquida e gassosa, idealmente a 1,9K dove ha il massimo di conducibilità. Si ottiene mettendo elio nella doppia parete, in contatto con lambda plate e He-I bifasico superiore. Basta 1 litro (=?). La conducibilità termica è 10^6 volte superiore e il problema della dissipazione è trasferito all’He bifasico, con lo stesso consumo. Così sparisce il problema del gas, rimane quello della potenza criogenica associata a quanta potenza di fascio si perde.
Meglio con compressori freddi (Linde ne fa a 4K) che con pompe, più affidabile anche se più costoso. Il tutto può costare 0,5 M€, da aggiungere al coasto dell’RFQ SC.

## Slide 44: Further comments
Construction challenges, different (EBW vs. brazing; cryogenic vs. high PRF issues…), not in severity
Construction tolerances (0,05 mm, for fres tuning) and alignment tolerances (0,2 mm) are achievable in both.
Develop a well cooled coupler. Locking issues due to low intrinsic bandwidth are no longer a problem; a 13 kW beam (Df=600 Hz) solves the problem with marginal increase of Ploss at 4K. A good coupler is required.
3. Cost: N-RFQ (SPES case, 80 MHz)=2,5 M€; for PIAVE S-RFQ (in 2018-€)=2 M€, no RM and bunching sections.
4. Other technologies could be considered: Nb/Cu (complex geometry, but much better mechanical stability); Pb/Cu (Hp ok, high enough Eacc possible?)
Notes: alignment tolerances=0,2 mm, achievable in both, determined predominantly by fres tuning; moreover 0,05 mm precision on 0,8 or 1,4 m weighs more than 0,1 mm on 4 m, so it is more relaxed than PIAVE SRFQs).
Cost: NC: 1M€ vanes, 0,5M€ tanks, 0,5M€ ancillaries, 0,5M€ RF = 2,5 M€ SC=?
f=80 MHz; at 2f, 4f worse field flatness, quadratically worse transverse focusing, Ea does not scale with f as it does with NC RFQ – Kilpatrick)
Errore di allineamento dovrebbe essere meno severo su una cavità più corta.

## Slide 45: Outlook
PIAVE S-RFQs at INFN-Legnaro have been working since 2006 for user operation
Further BCP, a better tuning system, LT alignment, improved gas He draining have improved their performance and reliability
A slightly modified design seems suitable for high-I beam acceleration, whether in full-Nb or Cu-based

## Slide 46: A dedication