## Slide 1: Cavity Failures and Beam Dynamics in the ESS Linac
Ciprian Plostinar on behalf of
Mamad Eshraqi, Yngve Levinsen, Ryoichi Miyamoto and Renato De Prisco
SLHiPP-8, 12-13 June 2018
Ångström Laboratory, Uppsala

## Slide 2: The ESS Linac
Ion Species | Protons | 
Output Energy | 2 | GeV
Frequency | 352.21/704.42 | MHz
Pulse Length | 2.86 | Ms
Peak Current | 62.5 | mA
Protons per Pulse | 1.1 x 1015 | 
Repetition Rate | 14 | Hz
Duty Cycle | 4 | %
Average Beam Power | 5 | MW
Accelerating Structures | RFQ, DTL, SC Spokes/Elliptical | 
Accelerator Length | ~365 | m

## Slide 3: The ESS Linac - Baseline Beam Dynamics
End-to-end Envelopes
RMS Emittance Evolution

## Slide 4: Cavity Failure Cases
Loss of field:
  Failure in the chain of high power RF
  Failure in cavity/environment
  Failure in control system
End-to-end muti-particle beam dynamics error studies (MEBT to A2T):
  Using beam distribution from RFQ simulation
  TraceWin/Partran
  Note the loss pattern rather than magnitude

## Slide 5: MEBT Cavities
Total losses in the whole linac in number of particles due to a complete failure of each MEBT lattice element, comparing the cases with and without the three MEBT scrapers.

## Slide 6: MEBT Cavities
Losses in linac due to complete failure of MEBT Bunchers. Losses into the three MEBT scrapers are not shown.

## Slide 7: DTL Tanks
Losses due to individual DTL tank RF failure

## Slide 8: SCL Cavities
Transmission for different cavity failure scenarios.

## Slide 9: SCL Cavities
Power lost for different cavity failure scenarios.

## Slide 10: SCL Cavities – with correction
Transmission after correction for the failed cavities. The reason Spoke 1 is not fully recovered is the “procedure used” for the correction. Using more cavities one can recover the beam in that case too.

## Slide 11: Transient Effects

## Slide 12: Assumptions
Sync phase stays constant
  valid for close to nominal field in the failing cavity
Cavity gets loaded by the beam at -50% of its operating voltage
  valid for cavities operating at the maximum of range, for lower voltages a value above |-50%| is closer to reality
The LLRF of the downstream cavities does not correct for delayed arrival
Losses are per microsecond, depending on the Q of the cavity and beam current, they should be scaled.

## Slide 13: Losses
SPK Cavity 1

## Slide 14: More Losses
SPK Cavity 1
SPK Cavity 11
SPK Cavity 26
MBL Cavity 1
MBL Cavity 36
HBL Cavity 1
HBL Cavity 40
HBL Cavity 84

## Slide 15: Predicting the loss – Minority Report
By looking at the amplitude and phase signal of the BPMs, beam loss/RF failure could be anticipated!
SPK Cavity 1

## Slide 16: Predicting the loss
SPK Cavity 1
SPK Cavity 11
SPK Cavity 26
MBL Cavity 1
MBL Cavity 36
HBL Cavity 1
HBL Cavity 40
HBL Cavity 84

## Slide 17: Is it detectable?
It depends on the modulation depth of the density required by the BPMs.
For 10% modulation, bunches with ~150 deg rms can be detected.
1% corresponds to ~200 deg RMS.

## Slide 18: Bunch length
SPK Cavity 1

## Slide 19: Bunch length
SPK Cavity 1
SPK Cavity 11
SPK Cavity 26
MBL Cavity 1
MBL Cavity 36
HBL Cavity 1
HBL Cavity 40
HBL Cavity 84

## Slide 20: Energy
SPK Cavity 1

## Slide 21: Energy
SPK Cavity 1
SPK Cavity 11
SPK Cavity 26
MBL Cavity 1
MBL Cavity 36
HBL Cavity 1
HBL Cavity 40
HBL Cavity 84

## Slide 22: Summary
Instant Failures
  MEBT:
    Bunchers: A large fraction of the beam actually reaches the target.
      MEBT scrapers largely ineffective for longitudinal losses.
  DTL:
    Considerable amount of losses inside Tanks 1 and 2 if Tank 1 is not at its nominal voltage.
  SCL:
    Depending on the energy at the failed cavity, the unaccelerated particles will be either lost locally or in the DogLeg.
Transient Effects
  Beam loss/RF failures could be predicted/detected before noticeable losses occur by looking at the amplitude and phase signal of the BPMs!
    Potential supplementary diagnostic information