## Slide 1: OVERVIEW OF THE ESS BEAM DIAGNOSTICS
Tom Shea
and the ESS Beam Diagnostics Team
Input from: C. Thomas, J. Norin, B. Cheymol, S. Molloy, R. Baron, H. Hassanzdegan, I. Kittelmann, T. Grandsaert, V. Grishin, H. Kocevor, C. Derrez,, M. Eshraqi, E. Adli, M. Poggi, M. Ferianis, I. Bustinduy, P. Aden, T. Papaevangenlou, J. Marroncle, L. Segui, S. Vilcins, A J. Johannson, and staff from virtually all partner and collaborating institutes.

## Slide 2: Outline
Overview
  Diagnostics Team Organization
  Beam Diagnostics Suite: Quantities and Scale
Systems Organized by Measurement Capability (highlighting only those in the superconducting linac)
  Beam Accounting
  Measurement of Beam Centroid
  Measurement of Beam Distribution
Protection
Outlook

## Slide 3: ESS Diagnostics: 22 Partners and Collaborators
Aarhus University
CEA Saclay, Paris
CERN, Geneva
Cockcroft Institute, Daresbury
DESY, Hamburg
Elettra – Sincrotrone Trieste
ESS Bilbao
INFN, Catania
INFN, Legnaro
Lund University
University of Oslo
Technical University of Denmark
Science and Technology Facilities Council, Daresbury
Warsaw University of Technology
IMP, China
J-PARC, Japan
Oak Ridge National Laboratory
Los Alamos National Laboratory
INR, Moscow
Högskola Väst, Trollhättan
Stony Brook U., New York
BNL, New York

## Slide 5: Scale
22 types of beam diagnostic systems
466 diagnostic systems with ~µs protection capability
>10000 tracked assets
~ 50 equipment racks in gallery
Tunnel: 514 diagnostic systems in the baselined lattice and shown in synoptic display
Stubs: 1740 long-haul cable runs (ion chamber BLM cables highlighted)
Gallery: 2260 named devices (rack-mounted electronic devices for ion chamber BLM highlighted

## Slide 6: Beam Accounting
Measuring beam current and where it is lost
  Constituents of beam extracted from ion source
  Losses that damage or activate accelerator
  Energy delivered to beam destinations
  Beam leaving aperture and overheating target/dump components
Systems
  Doppler
  Faraday Cups
  Beam Current Monitors
  Beam Loss Monitors
    Neutron detectors
    Ion chambers
  Aperture Monitors
To grave
From cradle

## Slide 7: Beam Accounting: Current Monitors
AC Current transformers in superconducting section
Integrated into vacuum flanged assembly
Signal handled by front end electronics before transmission to MTCA-based acquisition system.
~ mA accuracy, µs response

## Slide 8: Beam Accounting: Beam Loss
x
y
z
I. Kittelmann
In SCL: MARS simulation. dose from point loss @ 2 GeV
Neutron hit maps from GEANT4 for 3 different localized loss locations along the DTL tank1: possible correlation of the distribution peak position with the loss location
M. Jarosz
SCL GEANT4 simulations commencing with more detailed model
Photon background
X-Ray spectroscopy
Real-time background subtract
Particle discrimination
(SNS example)

## Slide 9: Beam Accounting: Neutron Detectors
Birmingham 40 MeV protons on Al
IPHI 3 MeV protons on Be
Draft of FPGA architecture
Neutron event detection
Handle pile-up and transition to current readout mode
Continuously buffered data acquisition with trigger system (Data on Demand – feature shared with other systems)
CEA, ESS-Lund, Łodz

## Slide 10: Beam Accounting: Ion Chamber Loss Monitors
All 285 detectors received summer 2017
Proton beam tests at CERN,
Gamma at LTH
Installed here in Uppsala for photon and EMI testing
Data transfer via API (in testing)
Data (HDF5), Device status in asset management system
Short pulse (5 us):  1% of 1 W/m

## Slide 11: Centroid Measurements: Beam Position and Phase
Button assembly manufacturing: DESY
Characterized and embedded in LWU at Daresbury

## Slide 12: Centroid Measurements: Beam Position and Phase
Focus on phase performance
Electronics, FPGA framework, non-IQ receiver design coordinated with LLRF team
Approximately 1 mA of beam
Approximately 0.1 mA of beam
S. Molloy, R. Baron, ESS Lund
Struck transition module, Digitizer w/Xilinx KU in MTCA
Also, custom RF front end

## Slide 13: Beam Distribution Measurements
Emittance Measurement Units
Wire Scanners
Bunch Shape Monitors
Non-invasive profile
Grid
Imaging

## Slide 14: Distribution Measurements: Invasive Profile: Wire Scanners, BSM
Grid Electronics: LTH
Linac wire scanner actuator: Århus; acceptance testing in RATS
Wire Scanner Electronics: Trieste
Bunch Shape Monitors: delivery complete from INR. A few ps resolution.
Clean room in Lund

## Slide 15: Distribution Measurements: Wire Scanner Electronics
EPICS and MTCA system integration
Analog electronics
Optical front end
Time resolved profile of Linac4 proton beam measured with ESS electronics and software
Trieste
Clement on WS (particle free, and test)

## Slide 16: Distribution Measurement: Measure Long Beam Pulses with Non-invasive Profile Monitors
NPM prototypes in beam at CEA
Ionization Profile Monitor
Saclay, ESS-Lund

## Slide 17: Protection from Beam Loss
  Total beam loss, ~µs latency required for protection
  BCM, icBLM (saturation), nBLM (current mode) -> Interlock
> 1.6 milliamp lost for up to 200 µs
  BCM, icBLM, nBLM -> Interlock
~ microCoulomb lost over 200 µs to diffusion time
  icBLM, nBLM -> Interlock
~ “1 Watt/meter” loss, dose management
  icBLM, nBLM -> alarm based on dose/activation plan
Before beam loss occurs, RF fault within pulse
  BPM -> Interlock before loss, based on change of energy
Position Monitors, and sparse coverage by Current Monitors
coverage by Ion Chambers
Neutron Detectors
FLUKA
ANSYS
Response of components to energy deposition by beam
Damage model:

## Slide 18: Differential Measurements
Bit error rate < 10**-15
3.125 Gb/s low latency link:
Developed for Beam Current Monitor
Capable of providing real-time communication between diagnostics, LLRF, neutron instruments, …
Current
Phase
Simulations by ESS Beam Physics

## Slide 19: Outlook Putting it all together
Acquisition
Analysis
Low latency processing
Continuous Buffering
Low latency data transmission
Updates to analysis layer managed by trigger system
Gigabit/s
Acquisition
Acquisition
Real-time Control and
Protection functions
Data analysis Machine learning
Adaptation
Machine
Actuators
Terabit/s
trig
trig

## Slide 20: Thank you