## Slide 1
Txema de la Fuente (JEMA)
www.europeanspallationsource.se
Critical Design Review on 660kVA klystron modulators for RFQ/DTL and MBeta
S3.4 – Central control system

## Slide 2
Central control system
Racks
Control. Racks.
CENTRAL CONTROL SYSTEM |  |  |  | 
Item |  | Manufacturer | Model | Features
06U11 | -- | NI | cRIO-9039 | DSP, FPGA
06U12,13,38 | -- | NI | NI-9220 | 16 AI
06U14,15,16,22,26,27,28,35 | -- | NI | NI-9401 | 8 DI/DO
06U52 | -- | NI | TPC-2230 | Screen
06U53 | -- | NI | NI Moxa EDS-G205-1GTXSFP-T | Ethernet switch
06U21,31 | -- | NI | NI-9149 | FPGA
06U23,24,25 | -- | NI | NI-9223 | 4 AI Diff
06U32,33,34 | -- | NI | NI-9482 | 4 SPST Relay
06U36U37 | -- | NI | NI-9425 | 32 DI

## Slide 3
Central control system
PCB
Control. PCB
CONTROL AND SIGNAL CIRCUITS (PCB) |  |  | 
Item |  | Manufacturer | Model
06U47 | -- | PROELEK/FALCON | Vmeas
06U43 | -- | PROELEK/FALCON | Imeas
06U44 | -- | PROELEK/FALCON | Pmeas
06U45 | -- | PROELEK/FALCON | Inv current
06U46 | -- | PROELEK/FALCON | Out I V
02U01….03U02 | -- | PROELEK/FALCON | IGBT splitter
06U41,42 | -- | PROELEK/FALCON | Log Itlk
02U11,31,51 | -- | PROELEK/FALCON | Crowbar
01U02…02U53 | -- | PROELEK/FALCON | PTC support
06U50 | -- | PROELEK/FALCON | Vmeter
04A11-U01…42 | -- | PROELEK/FALCON | HV rectifier
02U15,35,55 | -- | PROELEK/FALCON | Common mode filter
05U06 | -- | PROELEK/FALCON | RC snubber ARC
05U01 | -- | PROELEK/FALCON | IGBT adapter ARC
06U100 | -- | PROELEK/FALCON | External port

## Slide 4
Central control system
PCB
Voltage measurement board (Vmeas):
  Concentrate, adjust and condition the signals coming from the voltage analogue sensors and interface them to the central control system.
Current measurement board (Imeas):
  Concentrate, adjust and condition the signals coming from the current analogue sensors and interface them to the central control system.
Pulser measurement board (Pmeas):
  Concentrate, adjust and condition the signals coming from the different analogue sensors (voltage, current and others) and interface them to the central control system.
Inverter current measurement board:
  Conditioning of the analogue inverter current fast measurements.
Output current and voltage measurement board:
  Conditioning of the analogue output current and voltage fast measurements.
IGBT driver splitter board:
  Interface the IGBT control signals coming from the central control system and dispatch them to the different IGBT drivers.
Logic interlock board (Ltkl):
  Concentrate, adjust and condition the digital signals coming from the different components and interface them to the central control system.

## Slide 5
Central control system
PCB
Crowbar board:
  DC crowbar independent driver to manage and trigger the crowbar thyristor.
PTC support board:
  Mechanical and electrical conditioning of the PTC for measurements.
Voltage meter board (Vmeter):
  Adjust and condition the analogue measurement coming from the voltage sensors to visualize in the voltmeters.
Rectifier board:
  HV rectifier one leg for the HV module.
Common mode filter board (DC LV side):
  Resistor and capacitor network for the DC common mode filter.
RC snubber board (arc protection):
  RC snubber for the arc protection system IGBTs.
IGBT adapter board (arc protection):
  Interface electrical/optical with the arc protection system IGBT drivers.
External hardwired port board:
  Conditioning of the external interface signals: remote hard control port and external pulse trigger port.

## Slide 6
Central control system
Location
Control cabinet location

## Slide 7
Central control system
Racks
Control. Chassis #1

## Slide 8
Central control system
Racks
Control. Chassis #2

## Slide 9
Central control system
Racks
Control. Chassis #3

## Slide 10
Central control system
HMI
HMI:
  TPC-2230.
  15” Touch screen.
  Size: 307 x 383 mm.
  CPU Intel Atom E3827, 1.5GHz.
  TFT Led LCD
  Resolution: 1024 x 768 VGS

## Slide 11
Central control system
Internal signals
Control. Internal signal list.

## Slide 12
Central control system
Internal signals
Control. Internal signal list.

## Slide 13
Central control system
Internal signals
Control. Internal signal list.

## Slide 14
Central control system
External interface
Remote hard control port:
  Connection between modulator and external RF Local Protection System.
Remote fieldbus port:
  TCP/IP over Ethernet.
External trigger port:
  Independent connector for the trigger.
Local port:
  Monitoring of status, interlock, signals and parameters.