## Slide 1
ESS/ICS
Date: 2018-02-16
Control System
EPICS Client Software
Susanne Regnell

## Slide 2: Control System Studio
... is an Eclipse-based collection of tools to monitor and operate a large scale control system (EPICS)
  Display Builder
  Data Browser (live or archived data)
  Data Probe (to look at a specific value)
  Alarms Viewer (BEAST)
  Archiver Appliance
  Directory Service (also called Channel Finder)
  Save & Restore (Process Variable settings)
Official homepage: http://controlsystemstudio.org/

## Slide 3: The Architecture of EPICS
A Server provides information and service
A Client uses the service or asks for the information
For EPICS, client and server refer to their PVAccess role: i.e. PVAccess Client and PVAccess Server (PV = Process Variable)
This standard control system architecture is often called 3-tier architecture
  Client – Server – I/O
Network-based Client/Server Model
Process Variables communicated over computer network using PVAccess protocol
Client
PVA
Client
PVA
Server
PVA
Server
PVA
[Slide from Timo]

## Slide 4: Servers and Clients at ESS
10 Hz
1 Hz
0.1 Hz
100 Hz
1 kHz
10 kHz
100 kHz
1 MHz
10 MHz
Industrial automation (PLC)
Client(s)
PVA
Server
PVA
Server
PVA
Client
PVA
Server
PVA
Client
PVA
100 MHz
[Slide from Timo]

## Slide 5: CS-Studio (Display Builder) Operator Interface screens (OPIs) – EPICS Clients
Example of an OPI

## Slide 6: CS-Studio (Data Browser) EPICS Client

## Slide 7: CS-Studio (Data Probe) (EPICS Client)
Used to look at live values from
a single PV

## Slide 8: CS-Studio (Alarms Viewer) EPICS Client

## Slide 9: CS-Studio Channel Finder Directory service for EPICS Channels EPICS Client
Problem: EPICS has a flat name space
Solution: Generic Directory Service (Channel Finder)
EPICS clients need to know with which channel to communicate
Query for name, property value and tags associated with channels

## Slide 10: CS-Studio Save & Restore (EPICS Client)
”Save Sets” organised in folder structure.
Users maintain Save Sets, each defining an arbitrary number of PVs (channels).

## Slide 11: CS Studio Save & Restore
User presses ”Take snapshot”, current values from PVs in the Save Set are retrieved.
User presses ”Save snapshot” to commit the snapshot to the repository.
User presses ”Restore” to write values from snapshot to PVs.

## Slide 12: CS Studio Save & Restore
Two (or more) snapshots can be compared.

## Slide 13: Electronic Logbook
Logbook (Confluence pages)

## Slide 14: Other software
Open XAL framework for High level Physics applications (in production)
Post Mortem system (not started)
Operation Sequencer (not started)
Naming Service (Naming Convention) (in production)
Controls Configuration Database (in production)
Cable Database (in production)
IOC Factory (in production)
Calibration Service (under implementation)